Solar-Home-Systems

# General Overview

# Features

- The prices for Solar-Panels are lower than never before

- Solar-Panels have a normally a warranty of 20 years for about 85% of the Output-Power.

- System can be upgraded, that means start with a small system and then upgrade to a bigger system.

- The cost for electricity can be reduced

- No more Power-failure, safe Power-Supply. Can also be used as a emergency-Power-Supply

- Output-Voltage of the Inverter is very stable. Better than that of mains and no additional voltage-regulator are necessary.

- All parts are available in the country

- Car-batteries are not the first choice but can be used.

- Easy installation, but hardly by the consumer.

- Any device can be connected, but some devices do not make sense like air-condition, heating water etc.

- Also rechargeable NiCd or NimH-Batteries can be charged for torches etc.

- Mobile-Telephones can be charged

- People learn to save Energy, because they realize, that the battery is empty if they use too much energy.

- Almost maintenance-free

- “clean energy”, reduces CO2

- There is a sponsoring from the government for this kind of energy

# But

- The initial-costs are quite high

- Installation needs skilled personal

- Battery needs to be changed from time to time (for Solar-Battery 8-10 years)

- There are possibilities to extend life-time of the battery (Pulser, charge to 14,4V for a longer time etc)

# Options

- Only Solar: Everything is powered by Solar-Power.

- Solar and Mains. Using Solar Energy for all. The Inverter and System-Size has to be accordingly. Or there is a way to switch off high Energy-consumption Devices. Only if the Battery is empty switch to Mains. It could be a Relay connected to the Inverter. Manual switch by Inverter on/off. 
But during Power-failure may be the batteries are empty. A relay is required with 220 V coil and one NC and one NO-contact.

- Solar and Mains. Using Solar Energy only for some devices (like lamps etc). 
If the battery is empty there should be a switch to select Mains for this area. It could be automatically by a Relay connected to the Inverter-Output (A relay is required with 220 V coil and one NC and one NO-contact). But may be not all Solar Energy is used.

- Solar and Mains. Using Solar Energy only as Emergency-Backup-System. There should be an automatic switch over to Solar in case of Power Failure. Could be a Relay connected to Mains. But not all Solar Energy is used.

# What to consider

- CIS-Solar-Panel are more cheap, but they need about 15 % more space and it is said, that they did not last that long. Check guarantee-time should be 20 years.

- Solar-batteries are more expensive but last longer in a Solar-System

- The System should be open for future extensions.

- Automatic switch over the complete electricity in case of Power-failure requires a Power-Switch and an Inverter who can manage the whole consumption.

- There can be a second wiring and lamps for Solar and a manual or automatic switch over.

- If a fridge should be connected, a bigger size of the System is required.

- Air-Conditions are not applicable with the Solar-System, due to their high energy-Consumption.

- By Timer some devices can be switched on (fridge, washing etc) at the time of most sunshine.

# Requirements

- Should reduce Power-Consumption

- Should be a Emergency-Power-Supply in Case of Power-Failure

- Should be available in different sizes

- Should also promote rechargeable NiCd / NimH-Batteries for torches etc

- Should be shipped with Batteries which last long (no Gel-Type). Best is Solar-Type batteries.

- Solar-Panels should be fixed theft- and vandalism-protected

- Solar-Panels should have the right inclination (15 °C)

- People should be advised about refilling distilled water

- Distilled water should be available for the batteries

- Batteries should be protected for making a shortcut at the Poles

- Should be build up by locally available devices

- Parts should easy be replaced

- Not really necessary, but may be all be the equipment could be in a box for protection. The box should have openings for air going in and out.

- In case of problems, there should be somebody be mentioned to consult.

# How to finance?

- For example with a Solar Electricity-counter and the Consumer pays a monthly fee he has to pay for electricity as well – 15% for example.

- Rent and buy. Like above independent from the consumption

# Calculations

| Calculation Solar-System 300 W/ max 16A |  |  |
| --- | --- | --- |
|  | QTY | Unit | Total RS |  |
| SP 70 Watt CIS-Module | 4 | 4636,37 | 18545,48 | RS |
| Solar Module Stand | 8 | 295,31 | 2362,48 | RS |
| Bolts and Nuts | 16 | 23,62 | 377,92 | RS |
| 2,5 mm2 Wire Cable | 30 | 47,25 | 1417,5 | RS |
| Solar Charge Controller | 1 | 7594,13 | 7594,13 | RS |
| 4 Way-Wire Cable Junction box | 1 | 1937,25 | 1937,25 | RS |
| Solar Battery 100 Ah, 12V | 2 | 10000 | 20000 | RS |
| Lamps |  |  | 0 | RS |
| Switches |  |  | 0 | RS |
| Cable indoor wires |  |  | 0 | RS |
| Inverter 600VA | 1 | 6500 | 6500 |  |
| installation | 1 | 1500 | 1500 |  |
|  |  | Total | 60234,76 |  |

# What you can do with that?

| Number of | Consumer | Watt | Watt total | hours | Wh |
| --- | --- | --- | --- | --- | --- |
| 4 | Energy Saving Lamp | 13 | 52 | 4 | 208 |
| 4 | Energy Saving Lamp | 20 | 80 | 4 | 320 |
| 1 | Radio AC | 25 | 25 | 4 | 100 |
| 1 | Fan AC | 60 | 60 | 4 | 240 |
| 1 | TV | 50 | 50 | 4 | 200 |
|  |  |  |  | Total | 1068 |

| Calculation Solar-System 600 W |  |  |  |
| --- | --- | --- | --- |
|  | QTY | Unit | Total RS |  |
| SP 70 Watt CIS-Module | 8 | 4636,37 | 37090,96 | RS |
| Solar Module Stand | 16 | 295,31 | 4724,96 | RS |
| Bolts and Nuts | 32 | 23,62 | 755,84 | RS |
| 2,5 SQ mm Wire Cable | 40 | 47,25 | 1890 | RS |
| 4 SQ mm Wire Cable | 30 | 70,78 | 2123,4 | RS |
| Solar Management Unit | 1 | 7594,13 | 7594,13 | RS |
| 8 Way-Wire Cable Junction box | 1 | 2401,88 | 2401,88 | RS |
| Solar Battery 100 Ah, 12V | 4 | 4636,37 | 18545,48 | RS |
| Lamps |  |  | 0 | RS |
| Switches |  |  | 0 | RS |
| Cable indoor wires |  |  | 0 | RS |
|  |  |  | 0 | RS |
| Inverter 1000VA | 1 | 10000 | 10000 |  |
| installation | 1 | 6000 | 6000 | RS |
|  |  |  |  | RS |
|  |  | Total | 91126,65 | RS |

# What you can do with that?

| Number of | Consumer | Watt | Watt total | hours | Wh |
| --- | --- | --- | --- | --- | --- |
| 4 | Energy Saving Lamp | 13 | 52 | 4 | 208 |
| 4 | Energy Saving Lamp | 20 | 80 | 4 | 320 |
| 1 | Radio AC | 25 | 25 | 4 | 100 |
| 2 | Fan AC | 60 | 120 | 4 | 480 |
| 1 | TV | 50 | 50 | 4 | 200 |
| 1 | Fridge | 70 | 70 | 12 | 840 |
|  |  |  |  | Total | 2148 |

| Calculation Solar-System 1000 W |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | QTY | Unit | Total RS |  |
| SP 70 Watt CIS-Module | 14 | 4636,37 | 64909,18 | RS |
| Solar Module Stand | 28 | 295,31 | 8268,68 | RS |
| Bolts and Nuts | 56 | 23,62 | 1322,72 | RS |
| 2,5 SQ mm Wire Cable | 60 | 47,25 | 2835 | RS |
| 4 SQ mm Wire Cable | 30 | 70,78 | 2123,4 | RS |
| Solar Management Unit | 1 | 7594,13 | 7594,13 | RS |
| 8 Way-Wire Cable Junction box | 2 | 2401,88 | 4803,76 | RS |
| Solar Battery 100 Ah, 12V | 6 | 4636,37 | 27818,22 | RS |
| Combiner-Box | 1 | 3100,13 | 3100,13 |  |
| Lamps |  |  | 0 | RS |
| Switches |  |  | 0 | RS |
| Cable indoor wires |  |  | 0 | RS |
|  |  |  | 0 | RS |
| Inverter 2500 VA | 1 | 18000 | 18000 |  |
| installation | 1 | 3000 | 3000 | RS |
|  |  |  |  | RS |
|  |  | Total | 143775,22 | RS |

# What you can do with that?

| Number of | Consumer | Watt | Watt total | hours | Wh |
| --- | --- | --- | --- | --- | --- |
| 8 | Energy Saving Lamp | 13 | 104 | 4 | 416 |
| 8 | Energy Saving Lamp | 20 | 160 | 4 | 640 |
| 2 | Radio AC | 25 | 50 | 4 | 200 |
| 4 | Fan AC | 60 | 240 | 4 | 960 |
| 1 | TV | 50 | 50 | 4 | 200 |
| 1 | Fridge | 70 | 70 | 12 | 840 |
| 1 | Notebook | 50 | 50 | 4 | 200 |
|  |  |  |  | Total | 3456 |

26.3.2013

Stefan Schranner

Frau-Holle-Weg 28

97084 Würzburg

Telefon: +49 (0)931 72353

Mobil: +49 (0)152 54690448

Email: StefanSchranner@yahoo.de

Internet: www.alternative-technology.de